PRESS INFORMATION

22nd September 2008	For Immediate Release

LVPECL telecomms oscillator ensures 
high data integrity at fast transfer rates

Electronica, Munich, 11-14 November 2008: Hall B6, Stand 264 – IQD Frequency Products unveils a quartz crystal oscillator with complementary LVPECL (low-voltage positive emitter coupled logic) output, designed for use in telecommunications exchange equipment and other high-speed data switching applications. The new CFPS-59 SPXO (simple packaged crystal oscillator) is available with output frequencies from 75HMz right up to 170MHz.

The CFPS-59 provides very short signal rise and fall times of just 0.7 ns (20% to 80%), helping to ensure high data integrity even at today’s ever increasing data transfer rates. This figure compares with a typical rise/fall time for a low-cost HCMOS SPXO of perhaps 5 or 6 ns.

Specified for either industrial (–40( to +85(C) or general-purpose (–10( to +70(C) operating temperature range, the CFPS-59 offers frequency stabilities of 25, 50 or 100ppm. Devices are vibration qualified to Mil-Std-202F, making them suitable for use in industrial environments.

The CFPS-59 is housed in an industry standard six-pin 7 x 5mm SMD package and operates from a 2.5V supply. Tristate functionality is standard, and devices are available bulk packed or on tape and reel.

- Ends -

Notes for Editors:
Since its inception in 1973, IQD Frequency Products has established a leading position across Europe as a specialist supplier of quartz-based frequency control components. IQD offers one of the most comprehensive frequency product ranges available, from low-cost commercial-grade devices to those used in the most stringent military and professional applications. Its components, which are specified by leading manufacturers in the aerospace, communications, computing, consumer and medical industries throughout the world, include quartz crystals, crystal oscillators, programmable oscillators, VCXOs, TCXOs, OCXOs and rubidium standards. IQD takes a partnership approach to working with its customers. Specialist sales teams, assisted by an engineering led application support department, guide customers from initial design stage through to full production. IQD has external representatives and distributors in over 25 countries.

IQD Frequency Products Ltd recently acquired the Crewkerne (Somerset, UK) operations of Rakon Europe Ltd, following Rakon’s 2007 acquisition of the former Frequency Control Products division of 
C-MAC MicroTechnology.

Further information and enquiries:
Harriet Charles
IQD Frequency Products
T: +44 (0)1460 270200
E: harriet.charles@iqdfrequencyproducts.com
www.iqdfrequencyproducts.com

Issued by:
Andrew Taylor
AJT Communications
T: +44 (0)7966 398118
E: ajt-comms@zen.co.uk

IQD/002/D1